Annex

Ngong Ping Ropeway Stoppage Record

(from September 2006 to December 9, 2008)

| Date | Stoppage Duration | Reason |
| --- | --- | --- |
| September 30, 2006 | 10:35 – 11:26 (51 minutes) | An incorrect plug was used at Tung Chung Terminal, leading to improper functioning of the system. |
| October 8, 2006 | 16:48 – 17:46 (58 minutes) | Inadequate clearance between the hauling rope and the shaft of the rope catcher at the tower, ground fault alarm was activated. |
| October 15, 2006 | 10:00 –10:59 (59 minutes) | Delay in pre-operational arrangement |
| October 15, 2006 | 18:05 – 19:00 (55 minutes) | Inadequate cabin separation at Nei Lak Shan Angle Station |
| October 27, 2006 | 10:00 – 14:20 (4 hours 20 minutes) | Fault occurred at a conveyor inside the Cabin Storage Area |
| January 1, 2007 | 16:14 – 17:26 (1 hour 12 minutes) | A friction tire in Ngong Ping Terminal deflated |
| January 3, 2007 | 18:20 – 19:38 (1 hour 18 minutes) | Fault occurred at a speed encoder in Airport Island Angle Station |
| January 17, 2007 | 12:05 – 18:25 (6 hours 20 minutes) | Not taking required procedures corresponding to humid weather |
| April 9, 2007 | 18:05 – 18:56 (51 minutes) | Insufficient tension in a friction belt in Airport Island Angle Station |
| May 11, 2007 | 11:06 – 13:06 (2 hours) | Fault occurred at a damping roller in Tung Chung Terminal during operation |
| March 19, 2008 | 15:39 – 16:34 (55 minutes) | One of the friction belts in Ngong Ping Terminal dislodged. |
| March 29, 2008 | 14:59 – 15:29 (30 minutes) | One of the friction belts in Ngong Ping Terminal dislodged. |
| April 11, 2008 | 12:20 – 13:48 (1 hour 28 minutes) Note : 14:17 close of service (service resumed on April 12) | One of the friction belts in Nei Lak Shan Angle Station dislodged. |
| May 15, 2008 | 10:38 – 11:38 (1 hour) | Fault occurred at a speed encoder assembly in Nei Lak Shan Angle Station |
| June 26, 2008 | 14:05 – 14:40 (35 minutes) | Fault occurred at an electronic measurement device assembly in Nei Lak Shan Angle Station |

– End –