Table 1

| Emission Standard | 2007 | 2008 |
| --- | --- | --- |
|  | Number of Buses# | Emissions (tonnes)* | Number of Buses# | Emissions (tonnes)* |
|  |  | RSP | NOx | SO2 |  | RSP | NOx | SO2 |
| Pre-Euro | 609 | 20 | 280 | <10 | 482 | 20 | 230 | <10 |
| Euro I | 1,351 | 30 | 670 | <10 | 1,344 | 30 | 680 | <10 |
| Euro II | 2,711 | 40 | 900 | <10 | 2,695 | 40 | 920 | <10 |
| Euro III | 1,205 | 10 | 310 | <10 | 1,226 | 10 | 320 | <10 |
| Euro IV | 13 | <10 | <10 | <10 | 47 | <10 | 10 | <10 |

Remarks :		#	figures as at year end
					* 	rounded up to the nearest 10 tonnes

The annual changes in the emissions from franchised buses are due to various factors, such as vehicle mileage, replacement of buses, aging of in-use buses, and the progress of retrofitting buses with emission reduction devices, etc.  The levels of SO2 emitted from franchised buses have been very low since the switching to ultra low sulphur diesel or better motor vehicle diesel in 2001.